## Slide 1: Sewing Circuits
Angela Sheehan, Amanda Clark
Notes: One prebuilt of each circuit for each group, who has what experience?

## Slide 2: What we’re making today:
e-Textile Masks!

## Slide 3: E-Textiles * Sewable Circuits * Soft Circuits * Wearable Electronics

## Slide 4
Fabric and Fiber Arts, Traditional Craft, Fashion Techniques
Electronic Prototyping, Interaction Design, Computer Programming, Engineering
Becky Stern’s LilyPad Embroidery

## Slide 5
Why Use Sewable Electronics?
Washable
Easy to incorporate into overall design
Utilize sewing techniques vs soldering
Lightweight and small
LilyPad Arduino - programmable
A different way to approach electronics

## Slide 6
Materials
LilyPad LEDs
LilyPad Coin Cell Battery Holder - Switched
Coin Cell Battery
20mm (CR2032)
Conductive Thread
(Stainless Steel)

## Slide 7
Basic Circuit
Traditional Electronics
Sewable Electronics

## Slide 8
The Mask Circuit
Battery Holder
LED Boards
Negative Connections
Positive Connections

## Slide 9
What will it do?
Brainstorm, sketch, pseudocode (if using a microcontroller)
Plan your circuit
Map out placement of components and connections, sketch ideas.
Test it out
Test your hook ups and code before you sew! Alligator clips (or leaving the board snapped together) lets you test before sewing your project together.
Planning a Project

## Slide 10
Place components where you want them on your project - drawing a rough sketch on a piece of paper for general placement helps a lot.
With a pencil or chalk - draw the connections between components, these will act as your sewing guide.
Design Circuit Traces Before Sewing

## Slide 11
Sew conductive thread along your planned traces and loop through the conductive pads at least 3 or 4 times for a good connection.
More info: Sewing with Conductive Thread Tutorial
https://learn.sparkfun.com/tutorials/sewing-with-conductive-thread
Sewing Components

## Slide 12
Useful Tools
Multimeter
Small Pliers
Diagonal Cutters
Soldering Iron/Solder
Fray Check/Fabric Glue
Needle Threader
Embroidery Needles
Beeswax
Iron

## Slide 13
Connectors
Sewable Snaps
Magnets
Conductive Velcro
Zippers
Buckles/Clasps
You can use traditional craft findings to make detachable parts. Experiment with a multimeter and craft supplies to see what cool things you can use as connectors.
LilyPad Arduino
SimpleSnap
Image from LessEMF.com

## Slide 14
Beads used with conductive thread by Janet during a class at SparkFun https://www.sparkfun.com/news/533
LilyPad Arduino in an embroidery by Becky Stern http://sternlab.org/2008/04/lilypad-embroidery/

## Slide 15
http://web.media.mit.edu/~leah/LilyPad/build/turn_signal_jacket.html
Turn Signal Bike Jacket by Leah Buechley | 2008
LEDs to show when biker is turning, like car turn signals.

## Slide 16
http://www.diffus.dk/climate-dress/
Climate Dress by Diffus Design | 2009
Senses CO2 in the air and displays as light patterns

## Slide 17
http://www.instructables.com/id/musical-conductivity-detecting-light-up-hoodie/#intro
Soundie by Kanjun Qiu | 2009
A touch-sensitive light-up hoodie that makes sounds

## Slide 18: SparkFun E-Textile Tutorials
https://learn.sparkfun.com/tutorials/tags/e-textiles
https://learn.sparkfun.com/tutorials/firefly-jar
Firefly Jar Kit

## Slide 19: LilyPond project sharing site
http://lilypond.media.mit.edu/

## Slide 20: Basic Sewing Resources
http://www.kobakant.at/DIY
Lots of resources and experiments with soft circuit techniques.
Additional Resources
http://hlt.media.mit.edu/
MIT Media Lab focusing on crafting with technology.
How to thread a needle with a needle threader - cool animations!
http://www.wikihow.com/Thread-a-Needle-and-Tie-a-Knot
Types of stitches
http://diyfashion.about.com/od/diyfashion101/tp/Types-Of-Sewing-Stitches.htm

## Slide 21
Questions?

## Slide 22
www.sparkfun.com
6175 Longbow Drive
Boulder, Colorado 80301